## Slide 1
COMBUSTION IN POROUS MEDIA
Joshi Hrushikesh Ashutosh 20ME02002
Sanskaar Shrivastava 20ME02018
Vardhan Mittal 20ME02034
3rd Year Dual Degree
Under the guidance of
Dr. S. Kondaraju
School of Mehcanical Sciences
Indian Institute of Technology Bhubaneswar

## Slide 2
CONTENTS
  PROBLEM STATMENT
  GOVERNING EQUATIONS
  BOUNDARY & INITIAL CONDITIONS
  SET-UP
  ADVECTION VS. DIFFUSION
  NUMERICAL SCHEME & ACCURACY
  ALGORITHM
  RESIDUALS
  STABILTIY
  GRID INDEPENDENCE
  RESULTS
  PHYSICS

## Slide 3
FUEL + AIR
INLET
FUEL + AIR
OUTLET
POROUS MEDIUM
PIPE
PROBLEM STATEMENT
  A premixed air-fuel mixture enters the combustion pipe from the inlet.
  Inside the pipe is placed a plate made of porous material which serves as our porous medium.
  The air-fuel mixture undergoes combustion in the porous plate. Thus, the flame is held in the plate.
  Fresh air-fuel mixture continues to enter from the inlet and leave from the outlet after combustion.
SCHEMATIC OF THE SET-UP

## Slide 4
GOVERNING EQUATIONS
  The system can be modeled as two separate energy equations.
  The air-fuel mixture is treated as a homogenous gas while the porous medium is treated as a homogenous solid, both with constant properties.
  Combustion is modeled as a constant heat source term released at a certain location in the porous medium.
For the air-fuel mixture:
For the porous medium:

## Slide 5
BOUNDARY & INITIAL CONDITIONS
Initial Conditions:
  The porous plate and the air-fuel mixture are both at 473K.
Boundary Conditions:
  The inlet temperature is 473K
  The outlet is at zero temperature gradient.
BOUNDARY CONDITIONS OF THE SET-UP
INLET
(473K)
OUTLET
(Zero Temperature Gradient)
POROUS MEDIUM
(INITIALLY AT 473K)
AIR-FUEL MIXTURE (INITIALLY AT 473K)

## Slide 6
SET-UP
The values of the parameters used for the simulation are:
The simulation is run at three different velocities:

## Slide 7
  The governing equation for the air-fuel mixture have advection as well as diffusion terms.
  Depending upon the values of the set-up parameters along with the velocity of the air-fuel mixture, the system will either have advection or diffusion as the dominating factor.
  For analysis, the governing equations are non-dimensionalized and the values of the coefficients compared. Velocities above the threshold are advection dominant while below it are diffusion dominant.
ADVECTION VS. DIFFUSION
DIFFUSION
ADVECTION
For the air-fuel mixture:

## Slide 8
ADVECTION VS. DIFFUSION
Equating the coefficients of advection and diffusion terms:
For the values of:
The value of the non-dimensional velocity is:
The value of threshold velocity is:

## Slide 9
ADVECTION VS. DIFFUSION
DIFFUSION
  The porous medium does not have any advection terms.
  The porous medium has only diffusion.
For the porous medium:

## Slide 10
NUMERICAL SCHEME & ACCURACY
  The two differential equations have been discretized using forward time and central space (FTCS) scheme.
  Within the constraints of the problem, FTCS provides a computationally inexpensive and reasonably accurate way to simulate the system.
For the air-fuel mixture:

## Slide 11
NUMERICAL SCHEME & ACCURACY
For the porous medium:

## Slide 12
TYPE | VALUE
Air-Fuel Advection | 10^-4
Air-Fuel Diffusion | 7.87x10^-3
Solid Diffusion | 3.35x10^-4
STABILITY
  For stability analysis, CFL numbers are calculated.
  The most stringent number is 10^-4 and is taken as target and velocities chosen.

## Slide 13
  Make separate grids of the same resolution but different sizes for the solid and gaseous parts.
  Define the time step.
  Declare the boundary conditions.
  Select the value of the velocity as per advection or diffusion dominance.
  Discretize the equations using FTCS.
  For time step 'n', plug the required values in the discretized equations to get the values of temperature of the next step.
  Repeat step 6 from the 1st to the last time step.
ALGORITHM

## Slide 14
Node Number | Solid Residual Value (*10^-2) | Gaseous Residual Value (*10^-4)
5 | 8.5209696 | -1.6771823
60 | -0.0165757 | -1.6771320
92 | -1.5606060 | -8.3385744
RESIDUALS
  For the calculation of the residuals, the temperature data generated from the simulation is plugged into the original difference equations.
  The data is taken at three different nodes corresponding to the solid grid and the gaseous air-fuel mixture grid.
  The target was set as >0.1 and all the three test nodes satisfied the target for both grids.

## Slide 15
COLOUR | SOLIDxTIME
Blue | 50x100000
Red | 75x150000
Green | 100x200000
GRID INDEPENDENCE
  The simulation is run for 10^-3 m/s at 3 different resolutions.
  Maximum difference between two grid resolutions was 0.022K.

## Slide 16
GRID INDEPENDENCE
COLOUR | GASxTIME
Blue | 2000x100000
Red | 3000x150000
Green | 4000x200000

## Slide 17
Air-Fuel Mixture
Porous Medium
RESULTS
Velocity=10^-2 m/s

## Slide 18
Air-Fuel Mixture
Porous Medium
RESULTS
Velocity=10^-3 m/s

## Slide 19
Air-Fuel Mixture
Porous Medium
RESULTS
Velocity=10^-6 m/s

## Slide 20
PHYSICS
  The system is seen to have a spike in temperature for the gaseous phase as it passes through the porous medium.
  The rise in temperature is expected as the gas picks up heat from the flame in the porous medium.
  Sufficient length of pipe is taken to allow for temperature gradient to go to zero after the porous medium as is seen from the graphs.
  For the diffusion dominant case, the drop in temperature as diffusion takes over shows a smoother variation than for the advection dominant term.
  For the solid, the temperature profile is a concave downward curve as is expected because of the diffusion of heat in the entire solid.

## Slide 21
PHYSICS
  The faster the velocity, the more dominating is the advection part of the equation.
  Thus, to illustrate the dominance of advection over diffusion and vice-versa, the diffusion constants are changed by a factor of 1000 to allow for faster diffusion.
  Thus, the temperature gradient "smoothens-out" due to increased diffusion.
  It is to be noted that this is just a demonstration and does not hold any real world significance.

## Slide 22
THANK YOU